## Slide 1: Pentium FDIV bug
Team "Giant“

## Slide 2: The Pentium FDIV bug is a bug in the Intel P5 Pentium floating point unit (FPU)
Thomas Nicely - professor of mathematics at Lynchburg College, working on Brun’s Constant
October 24, 1994 – Thomas Nicely reported to Intel
November 7, 1994 – Bug go to press (Electronic engineering Times, CNN)
December 20, 1994, Intel offered to replace all flawed Pentium processors
A 1995 article in Science describes the value of number theory problems in discovering computer bugs

## Slide 3: This problem occurs only on some models of the original Pentium processor. Any Pentium family processor with a clock speed of at least 120 MHz is new enough not to have this bug.
Pentium P54C 600 nm 3.3V |  |  |  |  |  | 
Family | Model | Stepping | Core stepping | Clock rate | FSB speed | S-spec
5 | 2 | 1 | B1 | 75 MHz | 50 MHz | Q0601
5 | 2 | 1 | B1 | 90 MHz | 60 MHz | Q0542, Q0613, Q0543, SX879, SX885, SX909, SX874
5 | 2 | 1 | B1 | 100 MHz | 66 MHz | Q0563, Q0587, Q0614, SX886, SX910
5 | 2 | 2 | B3 | 75 MHz | 50 MHz | Q0606, SX951
5 | 2 | 2 | B3 | 90 MHz | 60 MHz | Q0628, Q0611, Q0612, SX923, SX922, SX921, SX942, SX943, SX944, SZ951
5 | 2 | 2 | B3 | 100 MHz | 66 MHz | Q0677, SX960

## Slide 4: The Pentium FDIV bug is the most famous of the Intel microprocessor bugs. It was caused by an error in a lookup table that was a part of Intel's SRT algorithm that was to be faster and more accurate.
Pentium P5 800 nm 5V |  |  |  |  |  | 
Family | Model | Stepping | Core stepping | Clock rate | FSB speed | S-spec
5 | 1 | 3 | B1 | 60 MHz | 60 MHz | Q0352, Q0412, SX753
5 | 1 | 3 | B1 | 66 MHz | 66 MHz | Q0353, Q0413, SX754
5 | 1 | 5 | C1 | 60 MHz | 60 MHz | Q0466, SX835, SZ949
5 | 1 | 5 | C1 | 66 MHz | 66 MHz | Q0467, SX837, SZ950

## Slide 5: At its worst, this error can occur as high as the fourth significant digit of a decimal number, but the possibilities of this happening are 1 in 360 billion. It is most common that the error appears in the 9th or 10th decimal digit, which yields a chance of this happening of 1 in 9 billion. Intel's lookup table consists of 1066 table entries, of which, due to a programming error, five were not downloaded into the programmable logic array (PLA)

## Slide 6: The presence of the bug can be checked manually by performing the following calculation in any application that uses native floating point numbers
The correct value is:
As a result the value returned by a flawed Pentium processor is incorrect
at or beyond four digits:

## Slide 7: $475 million